## Slide 1: Internet and HTTP
Software University
https://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Introduction to Internet
Important Definitions
HTTP Basics
URL
Tools for Developers
MIME
HTTP Request and HTTP Respond

## Slide 3: Have a Question?
sli.do
#python-web

## Slide 4: Introduction
An Introduction to the Internet

## Slide 5: What is the Internet?
Vast network that connects billions of devices together all over the globe
Through fiber optics, copper, satellites or cell phone network
We get indirectly connected though ISPs (Internet Service Providers)

## Slide 6: Networks and Internet
  Network is a group of two or more devices that can communicate
  The internet is made of hundreds of thousands of networks
  These different systems connect to each other, communicate with each other and work together because of standards for how data is sent

## Slide 7: Web Server Work Model
Request
Response
Web Server
Web Resources
HTML, PDF, JPG…
Web Client
Technology
Database

## Slide 8: Important Definitions

## Slide 9: Servers and Clients
  Servers are the machines that provide services to other machines
  Clients are the machines that are used to connect to those services

## Slide 10: Network Protocol
  Set of rules and standards, that allow communication between network devices
  Include mechanisms for devices to identify and make connections with each other
  Example for standard network protocols:
    TCP, UDP, IP, ARP
    HTTP, FTP, TFTP, SMPT, SSH

## Slide 11: Packets
Every message, file or stream of information sent over computer networks is broken down into small chunks called packets
Each packet contains important information inside of it called a header:
    Contents
    Origin
    Destination

## Slide 12: Internet Protocol (IP)
  All the devices on the Internet have IP Addresses
  Each IP address is unique to each computer or a device at the edge of the network
192.168.0.1
192.168.10.5
IP Address:
IP Address:

## Slide 13: IP Address
  An IP Address has many parts, organized in a hierarchy
  This version of IP Addressing is called IPv4
    Provides more than 4 billion 32 bits unique addresses
192.168.14.120
Subnetworks
Device address

## Slide 14: IP address classes

## Slide 15: Classless Inter-Domain Routing
CIDR is an IP addressing scheme that improves the allocation of IP addresses
Replaces the old system based on classes A, B, and C
Helps greatly extend the life of IPv4
CIDR | IP address range | Class
10.0. 0.0/8 | 10.0. 0.0 – 10.255. 255.255 | A
172.16. 0.0/12 | 172.16. 0.0 – 172.31. 255.255 | B
192.168. 0.0/16 | 192.168. 0.0 – 192.168. 255.255 | C

## Slide 16: IPv6
  IPv6 uses 128 bits
  Example of a full IPV6 address:
    3FFE:F200:0234:AB00:0123:4567:8901:ABCD
    The leading zeros can usually be left out
  Provides about 340 undecillion unique addresses

## Slide 17: Domain Name Server
  The domain name is a human way to access IP addresses for devices and websites around the world
  When a domain name is entered in the browser, a request is made the DNS
IP Address | Domains
216.58.214.46 | Google.com
217.174.159.195 | Softuni.bg

## Slide 18: Transmission Control Protocol (TCP)
Designed to send packets across the internet and ensure the successful delivery of data and messages over networks
Uses a process, where it looks at all the packets in a message and checks them
TCP verifies that all the packets are:
  In the right order
  Free of any issues
After that it certifies the data, and the packets are merged to recreate the original file that was on the sender's device

## Slide 19: TCP vs UDP
  TCP places reliability in a higher priority than speed
  For instances where reliability isn't as important, but speed is, there is another protocol called UDP (User Datagram Protocol)
  UDP doesn't do excessive reliability checks, but it can send information at a faster rate

## Slide 20: Open System Interconnect Model
OSI Model consists of 7 layers
  Each layer serves the layer above it and in return, it is served by the layer below it
Understanding each layer of the model helps us with:
  Troubleshooting
  Communicating better with technical and non-technical individuals about any system

## Slide 21: OSI Layers
OSI Model consists of 7 layers:
Example Protocols
HTTP, DNS, FTP, SMTP
TLS, SSL, compression
NetBIOS, PPTP, Sockets
TCP, UDP
IP, IPsec
ATM, Ethernet, MAC, LLC
USB, Bluetooth, 802.11a/b/g/n

## Slide 22: Basic Hardware Components
Cables - transfer data from one device to another
Routers - transfer data packets between different computer networks (operates on level 3 of OSI)
Repeaters, Hubs and Switches - connect network devices together so that they can function as a single segment
Network Interface Card (NIC) - computer component that connects the device to the network

## Slide 23: HTTP Basics
Web Communication Explained
http://

## Slide 24: Hyper Text Transfer Protocol
HTTP
TCP
IP
Ethernet
HTTP
TCP
IP
Ethernet
Media (wires / air / fiber)
Request
Response
Notes: HTTP == Hyper Text Transfer Protocol
  Client-server protocol for transferring Web resources (HTML files, images, styles, scripts, data, etc.)
  The widespread protocol for Internet communication today
  Request-response model (client requests, server answers)
  Text-based format (human readable)
  Relies on unique resource URLs
  Provides resource metadata (e.g. encoding)
  Stateless (cookies and Web storages can overcome this)

## Slide 25: HTTP Request Methods
Method | Description
POST | Create / store a resource
GET | Read / retrieve a resource
PUT | Update / modify a resource
DELETE | Delete / remove a resource
The four basic functions of persistence storage.
Other HTTP Methods
CONNECT
HEAD
OPTIONS
TRACE

## Slide 26: HTTP Conversation: Example
HTTP request:
HTTP response:
HTTP/1.1 200 OK
Date: Mon, 5 Jul 2010 13:09:03 GMT
Server: Microsoft-HTTPAPI/2.0
Last-Modified: Mon, 12 Jul 2014 15:33:23 GMT
Content-Length: 54
<CRLF>
<html><title>Hello</title>
Welcome to our site</html>
The empty line denotes the end of the response headers
GET /courses/javascript HTTP/1.1
Host: www.softuni.bg
User-Agent: Mozilla/5.0
<CRLF>
The empty line denotes the end of the request headers

## Slide 27: What's HTTP/2.0
Major revision of the HTTP network protocol used by the World Wide Web
  Supported by most of the popular web browsers
Fast and optimized, meets modern web usage requirements
Completely Backwards-Compatible
As of Jan 2021, almost 50% of all the websites support HTTP/2 (W3Techs statistics).

## Slide 28: URL
Uniform Resource Locator

## Slide 29: Uniform Resource Locator (URL)
A URL is a reference to a web resource that specifies its location on a network and a mechanism for retrieving it
A URL is a specific type of URI (Uniform Resource Identifier)
Protocol
Host
Port
Path
Query String
Fragment
http://localhost:8080/demo/index.html?id=27&lang=en#lecture

## Slide 30: URL Encoding
URLs are encoded according RFC 1738:
  Safe URL characters: [0-9a-zA-Z], $, -, _, . , +, *, ', (, ), ,, !
All other characters are escaped by:
  Space is encoded as "+" or "%20"
  URL-encoded string:
%[character hex code]
%D0%9D%D0%B0%D0%BA%D0%BE%D0%B2-%E7%88%B1-SoftUni
Наков-爱-SoftUni
Char | URL Encoding
space | %20
щ | %D1%89
" | %22
# | %23
$ | %24
% | %25
& | %26

## Slide 31: Tools for Developers
Dev Tools

## Slide 32: Tools for Developers – Browser Dev Tools
Chrome Developer Tools
Mozilla Developer Tools

## Slide 33: Tools for Developers – Browser Add-ons
Postman - Chrome
Rested - Firefox
</>

## Slide 34: Multi-Purpose Internet Mail Extensions
MIME and Media Types

## Slide 35: What is MIME?
MIME == Multi-Purpose Internet Mail Extensions
  Internet standard for encoding resources
  Originally developed for email attachments
  Used in many Internet protocols like HTTP and SMTP

## Slide 36: Common MIME Media Types
MIME Type / Subtype | Description
application/json | JSON data
image/png | PNG image
image/gif | GIF image
text/html | HTML
text/plain | Text
text/xml | XML
video/mp4 | MP4 video
application/pdf | PDF document

## Slide 37: HTTP Request / HTTP Respond

## Slide 38: HTTP Request Message
Request message sent by a client consists of:
  HTTP request line
    Request method (GET / POST / PUT / DELETE / …)
    Resource URI (URL)
    Protocol version
  HTTP request headers
    Additional parameters
  HTTP request body – optional data e.g., posted form fields
<method> <resource> HTTP/<version>
<headers>
(empty line)
<body>

## Slide 39: GET Request Method – Example
<form method="get">
Name: <input type="text" name="name" />
Age: <input type="text" name="age" />
<input type="submit" />
</form>
GET /HTTP/1.1
Host: localhost
<CRLF>
HTTP request line
HTTP request headers
The request body is empty

## Slide 40: POST Request Method – Example
POST /login HTTP/1.1
Host: localhost
Content-Length: 59
<CRLF>
username=mente&password=top*secret!
<CRLF>
HTTP request line
HTTP request headers
The request body holds the submitted form data
The POST method transfers data in the HTTP body
POST can send text and binary data e.g., upload files

## Slide 41: HTTP Response Message
The response message sent by the HTTP server consists of:
  HTTP response status line
    Protocol version
    Status code
    Status text
  Response headers
    Provide meta data about the returned resource
  Response body
    The content of the HTTP response (data)
HTTP/<version> <status code> <status text>
<headers>
<CRLF>
<response body – the requested resource>

## Slide 42: HTTP Response Codes
HTTP response code classes
  1xx: informational (e.g., "100 Continue")
  2xx: successful (e.g., "200 OK", "201 Created")
  3xx: redirection (e.g., "304 Not Modified", "301 Moved Permanently", "302 Found")
  4xx: client error (e.g., "400 Bad Request", "404 Not Found", "401 Unauthorized", "409 Conflict")
  5xx: server error (e.g., "500 Internal Server Error", "503 Service Unavailable")

## Slide 43: HTTP Response – Example
Example of HTTP response from the Web server:
HTTP/1.1 200 OK
Date: Fri, 17 Jul 2010 16:09:18 GMT+2
Server: Apache/2.2.14 (Linux)
Accept-Ranges: bytes
Content-Length: 84
Content-Type: text/html
<CRLF>
<html>
<head><title>Test</title></head>
<body>Test HTML page.</body>
</html>
HTTP response status line
HTTP response headers
HTTP response body

## Slide 44: HTTP Response – Example
Example of HTTP response with error result:
HTTP/1.1 404 Not Found
Date: Fri, 17 Nov 2014 16:09:18 GMT+2
Server: Apache/2.2.14 (Linux)
Connection: close
Content-Type: text/html
<CRLF>
<HTML><HEAD><TITLE>404 Not Found</TITLE></HEAD>
<BODY>
<H1>Not Found</H1>
The requested URL /img/logo.gif was not found on this server.<P> <HR><ADDRESS>Apache/2.2.14 Server at Port 80</ADDRESS>
</BODY></HTML>
HTTP response status line
The HTTP
response body
HTTP response headers

## Slide 45: Browser Redirection
HTTP GET requesting a moved URL:
The following HTTP response (301 Moved Permanently) tells the browser to request another URL:
GET / HTTP/1.1
Host: http://softuni.org
User-Agent: Gecko/20100115 Firefox/3.6
<CRLF>
HTTP/1.1 301 Moved Permanently
Location: http://softuni.bg
...

## Slide 46: Content-Type and Disposition
With Content-Type response header the server specifies how the output should be processed
Examples:
Content-Type: text/html; charset=utf-8
Content-Type: application/pdf
Content-Disposition: attachment; filename="Report-April-2016.pdf"
UTF-8 encoded HTML page. Will be shown in the browser.
This will download a PDF file named Report-April-2016.pdf

## Slide 47: Summary
…
…
…
Internet, Definitions of Internet
Sending and Receiving Information
What is HTTP
What is URL
Browser Tools for Developers
What is MIME

## Slide 48: Questions?
Notes: 48

## Slide 49: SoftUni Diamond Partners

## Slide 50: Educational Partners

## Slide 51: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 51

## Slide 52: License
This course (slides, examples, demos, exercises, homework, documents, videos and other assets) is copyrighted content
Unauthorized copy, reproduction or use is illegal
© SoftUni – https://about.softuni.bg/
© Software University – https://softuni.bg
Notes: 52